## Slide 1: Estimation of Background Noise Based on Excitation Patterns in Cochlear Implants
Opening Proposal of Student Research Project
Fang Xiao, B.Sc.
Reemt Hinrichs, M.Sc. (TNT)
Max-Heinrich Laves, M.Sc. (IMES)
Prof. Dr.-Ing. Tobias Ortmaier (IMES)
Prof. Dr.-Ing. Jörn Ostermann (TNT)
Institut für Informationsverarbeitung
Leibniz Universität Hannover

## Slide 2: Overview
Structure
Introduction
Background
Motivation
Progress So Far
General Ideas
Candidate Algorithms (Preliminary Results)
EP-based modification
Future Plans
Testing Scenarios
Statistical Evaluation
Timetable

## Slide 3: Introduction
Cochlear Implant (CI)
Components: microphone, speech processor and electrodes.
Limitation: intelligibility decreases in non-stationary environments.
Binaural sound coding strategy (BSCS, Gajecki et al., 2018)
2
Source: https://www.csun.edu/ncod/cochlear-implants
Notes: What’s CI; Components
Limitations: Noise, Battery
BSCS: Master/ Slave model; EP-based
Motivation: compare by EP
SCS (EP intro):

## Slide 4: Introduction
Cochlear Implant (CI)
Components: microphone, speech processor and electrodes.
Limitation: intelligibility decreases in non-stationary environments.
Binaural sound coding strategy (BSCS, Gajecki et al., 2018)
3

## Slide 5: Introduction
Choice: Advanced Combinational Encoder (ACE)
Illustration (part one): from audio signals to envelope
4
Sound coding strategy

## Slide 6: Introduction
5
Choice: Advanced Combinational Encoder (ACE)
Illustration (part two): from envelope to excitation patterns (EP)
Sound coding strategy

## Slide 7: Overview
Structure
Introduction
Background
Motivation
Progress So Far
General Idea
Candidate Algorithms
EP-based modification
Future Plans
Testing Scenarios
Statistical Evaluation
Timetable

## Slide 8: Progress So Far
General Idea
7

## Slide 9: Progress So Far
Candidate Algorithms
8
1. Improved Minimum Controlled Recursive Averaging (IMCRA, Cohen, 2003)
Estimation by recursive averaging with “soft decision” (speech presence probability, or “SPP”)
Minimum-controlled estimation with two orders of smoothing
2. MMSE-based Noise PSD Tracking (MMSE-BC, Hendricks et. al, 2010)
Bias Compensation
Safety Net
3. Unbiased MMSE-based Noise Power Estimation (MMSE-SPP Gerkmann et. al, 2012)
Use of “soft decision” avoiding BC and safety net

## Slide 10: Candidate Algorithms
Fang Xiao
xiaofang@tnt.uni-hannover.de
IMCRA [Cohen,2002]
9
Notes: Move equations to Backup

## Slide 11: Progress So Far
Candidate Algorithms
10
1. Improved Minimum Controlled Recursive Averaging (IMCRA, Cohen, 2003 )
Estimation by recursive averaging (with “soft decision”)
Minimum-controlled estimation
2. MMSE-based Noise PSD Tracking (MMSE-BC, Hendricks et. al, 2010)
Bias Compensation
Safety Net
3. Unbiased MMSE-based Noise Power Estimation (MMSE-SPP, Gerkmann et. al, 2012)
Use of “soft decision” avoiding BC and safety net
Notes: Full name of abbr.!

## Slide 12: Candidate Algorithms
MMSE-BC [Hendricks, 2010]
11

## Slide 13: Progress So Far
:Candidate Algorithms
12
1. Improved Minimum Controlled Recursive Averaging (IMCRA, Cohen, 2003)
Estimation by recursive averaging (with “soft decision”)
Minimum-controlled estimation
2. MMSE-based Noise PSD Tracking (MMSE-BC, Hendricks et. al, 2010)
Bias Compensation (BC)
Safety Net
3. Unbiased MMSE-based Noise Power Estimation (MMSE-SPP, Gerkmann et al., 2012)
Use of “soft decision” avoiding BC and safety net

## Slide 14: Candidate Algorithms
Almost identical procedures to the MMSE-BC
Rough decision → “soft weighting”
MMSE-SPP [Gerkmann, 2012]
13

## Slide 15: Progress So Far
EP-based Modification
14
N-of-M selection causes information loss
EP instead of audio signals as input
Treated as a special kind of PSD

## Slide 16: Preliminary Results
Original Audio Signals
15

## Slide 17: Preliminary Results
Audio-based Noise Estimation
16

## Slide 18: Preliminary Results
EP-based Noise Estimation
17

## Slide 19: Preliminary Results
Rough Comparison
18

## Slide 20: Overview
Structure
Introduction
Background
Motivation
Progress So Far
General Idea
Candidate Algorithms
EP-based modification
Future Plans
Testing Scenarios
Statistical Evaluation
Timetable

## Slide 21: Future Plans
Further testing factors：
Stimulation rate: “N-of-M” selection
Band selection: rough prediction
The typical influencing factors of noises:
Noise types: CCITT, Office, etc…
Noise levels: constant / variant in segments
Real-world position simulation
Multiple noise sources (“Cocktail party effect”)
“Codec-introduced” noise
Testing Scenarios
20

## Slide 22: Future Plans
Evaluation
21
Estimation Accuracy
Segmental SNR
Log-error distortion measure
Statistical Evaluation
Standard error
Confidence interval
Notes: Explain!
In words (definition; how it works in comparing process)
Equation in Backup

## Slide 23: Timetable
Timetable (planned) | 
Official Start: 11.11.2019 Official Deadline: 10.05.2020 | 
01.Nov – 30.Nov (2019) | Literature review; Code implementation of the first algorithm of noise estimation
01.Dec – 31.Dec | Code implementation of two other algorithms; Perform preliminary comparison
01.Jan – 31.Jan (2020) | Designing testing scenarios and statistical evaluation; Verifying further possibilities of EPs
01.Feb – 29.Feb | Performing testing scenarios; Statistical evaluation; Refining the codes.
01.Mar – 31.Mar | Formulate the thesis

## Slide 24: Backup
23
Detailed ACE Process

## Slide 25: Backup
24
Complex Gaussian Distribution Assumption
& MMSE-Estimator (Bayes’ Rule)

## Slide 26: Backup
25
Maximum-Likelihood Estimation of a-priori SNR
Gain Function Modified in IMCRA
Decision-Directed Approach of a-priori SNR

## Slide 27: Backup
26
Log-Error Distortion Measure
Segmental SNR

## Slide 28: Progress So Far: Candidate Algorithms
Fang Xiao
xiaofang@tnt.uni-hannover.de
IMCRA [Cohen,2002]
27
Two order of recursive averaging in both T-F domain
Soft decision: speech presence
Noise Estimation, integrated with SPP-based smoothing
Rough decision:
strong noise identification
Notes: - DETAILED FLOW CHARTS!
- Move equations to Backup

## Slide 29: Progress So Far: Candidate Algorithms
MMSE-BC [Hendricks, 2010]
28
MMSE-estimation of noise power
Direct-decision approach
for a-priori SNR estimate
Bias compensation
and safe net
- Bayes’ rule
- Complex Gaussian distribution assumption for noise and speech power